## Slide 1: The Association between Precipitation Intensity and Traffic Speeds
Final Project
Author: W. Logan Downing

## Slide 2: Outline
Primary Questions of this Analysis
The Data Sources
Interpolation
Analysis
Conclusions

## Slide 3: Primary Questions of this Analysis
What impact does precipitation intensity have on traffic speeds?
  How different (if at all) are traffic speeds under precipitation conditions compared to dry conditions and to what extent?
  Is there a spatial or temporal relationship between traffic speeds and precipitation intensity?
  Are there external factors that influence the traffic speeds that can be determined from the data?

## Slide 4: The Data Sources - Traffic
Traffic speeds will be sourced from the INRIX speeds database maintained by Purdue’s JTRP. All speeds are from June 2018.
    1-minute resolution down sampled to 2-minutes.
    These are remotely collected and crowd-sourced average traffic speeds.
      300 million data sources (http://inrix.com/research/).
    Consist of High, Medium, and Low confidence speed estimates.

## Slide 5: The Data Sources - Traffic
This study will focus on the I-65 North Bound corridor from Zionsville to Lafayette Indiana and consists of 69 segments.
Low Confidence | Medium Confidence | High Confidence
0% | 1.25% | 98.75%
Traffic Direction
Notes: Confidence score percentages are derived from the 1 minute data.
High confidence is real time data.
Medium confidence data is computed from surrounding segments (likely real time)
Low confidence is historical data.
Takes out the difficult problem of imputation for missing data.

## Slide 6: The Data Source – Precipitation Intensity
The weather data comes from the National Severe Storms Laboratory’s Multi-Radar Mutli-Sensor system. The data in this analysis is courtesy of the Iowa Environmental Mesonet. All precipitation data is from June 2018.
  1km x 1km grid spacing.
  2-minute temporal resolution.
  Derived from a combination of radar, observations (upper-air, satellite, ground), and forecast models.

## Slide 7: Interpolation
The first problem to solve: Getting precipitation estimates at the road segment level.
  This was accomplished using the interpp function from the akima package.
    The function performs bilinear interpolation.
100 | 133 |  | 200
 | 164.3 |  | 
220 | 180 |  | 100
2/3 * 100 + 1/3 * 200
2/3 * 220 + 1/3 * 100
2/3 * 180 + 1/3 * 133
The x-direction comes first, followed by the y-direction.
Notes: Process takes roughly 6 hours.
Other methods of interpolation like Kriging were considered but were ultimately deemed entirely too slow for the constraints of this project.

## Slide 8: The Analysis – Defining Terms
To start analyzing anomalies in the traffic data, it was important to establish a sort of normal. Normal traffic flow was defined as follows.
  Greater than or equal to 60 mph is considered normal traffic speeds.
We’re specifically interested in events where traffic slows down and precipitation is non-zero.
  Situations where speeds are less than 60 mph and precipitation intensity is above 0 are considered an “Event”

## Slide 9: The Analysis – Defining Terms
A temporal component to this relationship is suspected.
  Day and Night have been defined based on civil twilight hours for June 2018 in Indiana.
    Day: 6:00 am to 8:30 pm (1000 UTC – 0030 UTC)
    Night: 8:31 pm – 5:59 am (0031 UTC – 0959 UTC)

## Slide 10
Notes: Traffic Speeds under Normal Conditions Vs. Slow Downs with Day and Night Highlighted.
The data has been diced up into day and night as well as events with precipitation > 0 and speeds < 60 and usual traffic > 60 mph.
What is revealed in this plot is that the traffic speeds seem to be somewhat resistant to precipitation intensity impacting speeds.
Another notable point of interest is the significant number of events that occur during the night compared to the day time. This goes against the assumption
I originally held that due to low volumes, traffic speeds should be mostly unimpeded by precipitation intensity at night but is somewhat intuitive
Due to visibility constraints.
This answers the question of whether or not there is a temporal component to the relationship between traffic speeds and precipitation intensity as it does
Appear that there is some form of a relationship here. Now to quantify that relationship and see if there is a spatial component as well.

## Slide 11: Analysis - Developing Statistics on the Data
Using these day/night and event/non-event criterions, the following statistics have been produced.